Different length of sports tracks the sports stadium.

Practical demonstration of Mathematics.

It is certain that each track on sports stadium is different length  .

If athletes want to run only one round   and they are in different tracks , they can not start on one line.

Let's calculate the difference   length of tracks.

We must know the width of a single track.

So counting:

Circumference   is   π x d  = 3,14 x 41 = 128,74 m              d is diameter circle

Perimeter first running track is  ......128,74 + 60 + 60 = 248,74 m     approximated    249 m.

Width of one track is 1,2 m, after that  perimeter second (next) track is :

π x ( d + 2,4)  =  π x d    +    π x 2,4  = 128,74 m+ 7,54 m  =  136,28 m

Perimeter:             60 + 60 + 136,28 m  = 256,28 m.

So the difference   length of tracks is 7,54 m.

Mária Debnárová BellAmos Martin Slovakia