ERASMUS

STUDY OF THE FRAME

Functional specifications

FP1 : Connect all the organs of the vehicle on the road

FP2 : Protect the driver of the outside environment

FC1 : Respect the regulations

FC2 : Resist the attacks of the outside environment

FC3 : Participate in a good stability on the road

FC4 : Must be adapted to the user

FC5: Assure the connection of all the components

FC6 : Limit manufacturing costs and of use

To respect the imperatives bound to the functions FC3 and FC6, we settle the following criteria:

| Mark | Function | Criterion of appreciation | Level |
| --- | --- | --- | --- |
| FC3 | Participate in a good stability on the road | Displacement Maxi stress | 3 mm 25 Mpa |
| FC6 | Limit the costs to the use | Mass | Less than40 kg |

STUDY OF PROFILES AND MATERIALS

Complete the picture(board) this below highlighting the various resistances according to profiles and materials (see secondary 1).

| Profiles | Materials | Mass (Kg) | Elastic resistance (Mpa,N/mm²) | Stress (Mpa,N/mm²) | Displacement (mm) |
| --- | --- | --- | --- | --- | --- |
| 30x30 | Plein carbon stell |  | 220 MPa |  |  |
| 30x30 | 5086 Alu |  | 76 MPa |  |  |
| 40x40 | Plein carbon stell |  | 220 MPa |  |  |
| 40x40 R | Plein carbon stell |  | 220 MPa |  |  |
| 40x40 | 5086 Alu |  | 76 MPa |  |  |

In the reading of the results(profits), what profile corresponds at best to the specifications?

______________________________________________________________________________________________________________________________________

INFUENCE OF THE GEOMETRY OF THE FRAME

We are going to study the influence that a structure with triangulation with regard to a classic structure can have.

We shall use in both cases the same profile and the same material under an identical load.

Open by means of solidworks the file "structure" then proceed in the same way as previously

| Geometry | Mass (Kg) | Stress (Mpa,N/mm²) | Displacement (mm) |
| --- | --- | --- | --- |

Which is the most resistant geometry ?

______________________________________________________________________________________________________________________________________

Let us study the influence that a reinforcement on the deformation of the frame can have.

Open the file " modified frame V6 with reinforcement with "solidworks 2014/2015" and study the following profile

| Profiles | Materials | Mass (Kg) | Elastic resistance (Mpa,N/mm²) | Stress (Mpa,N/mm²) | Displacement (mm) |
| --- | --- | --- | --- | --- | --- |
| 40x40 R | 5086 Alu |  | 76 MPa |  |  |

This structure answers it the constraints put during the specifications?

______________________________________________________________________________________________________________________________________

SECONDARY 1

Open the file " modified frame V6 with reinforcement"  with solidworks 2014/2015

DISPLAY OF THE RESULTS

Proceed in the same way to study the other configurations

# Text boxes

Frame

Cost

Organs of the vehicle

Driver

Regulation

Environment

Road

FP1

FP2

FC1

FC2

FC3

FC4

FC5

FC6

1-In the menu solidworks choose  tools  then click  add-ins

2- Choose solidworks simulation then click ok

1- Select the  configuration 30x30 plein carbon steel

2-Make a right click on  30x30 plein carbon steel   then select  Activate SW configuration

3- Click on run

Make a right click on stress then select show

Make a right click on displacement then select show

Click on mass properties