## Slide 1
Surviving the Death Loop
(Etwinning Project)

## Slide 2: Lab report
Aim: we are going to verify from which height it is enough to start to do a complete loop.
Materials: - track
  - car
  - meter

## Slide 3
EtotA = Epot A
EtotC = Ekin+Epot = ½ * m *V2 + m * g * 2R
(as we have already said, the centripetal force must be bigger than the weight force)
m * v2 / R > m* g (we obtain that m*V2 > m*g*r)
There’s an energy conservation so we can equalize the 2 formulas.
m*g*h = ½ *m*v2 + m*g*2R (we replace)
m*g*h> ½ *m*g*R + 2*m*g*R
m*g*h> ½ *m*g*R+ 4/2*m*g*R
m*g*h> 5/2*m*g*R
h> 5/2*R
C
Introduction The most important point of the experiment is point “C”, where the car must have a precise amount of strenght not to fall. This strenght is called centripetal force and it has to be bigger than the weight force.
Let’s find out the height !
A

## Slide 4
Conclusion: so do a complete loop, the height must be larger than 5/2*R (THIS IS VALID ONLY WITHOUT FRICTION )
Group 2
Francesca Miola, Camilla Bendandi, Nicola Balbi, Simone Ricuperati and Giulia Tusone
To see a real DEATH LOOP, come to visit us and go to MIRABILANDIA!
Click here to see!