The table construction

Step 1 : what do we need ? / 3 square cut timbers 70 x 70 x 3000 / 2 wooden planks 195 x 26 x 3000 / 1 wooden plank 95 x 26 x 3000 / 8 metal squares. / 2 nuts bolts and rings / 2 metal plates / 70 mm screws (32) – 50 mm screws (72) / a saw - a pencil - a measuring tape - a square tool – a 60° mesuring tool - a drill – a long 10 mm drill bit - a 25 mm drill bit - a small drill bit (D3) - a milling drill bit - sand paper	Step 2 : the structure, first cuts. / Cut the timbers / Mind the square cuts

Step 3 : the structure, place the pieces / Place the 1754, 870 and the 600 mm pieces as shown above. / Cut the 1754 piece ends with a 60° angle. / Place the 850 mm piece, trace and cut the extra bits	Step 4 : the structure, fix the legs / Fix each leg (654 mm) with 2 metal squares and 50 mm screws (12)

Step 5a : the structure, fix the sides. / Drill a 20 mm deep hole with a large bit (25). / Step 5c : / Drill a 2 cm deep hole with a large bit (25)	Step 5b : / Drill the side with a long 10 mm drill bit. Make sure you drill through the 2 timbers / Step 5d : / Fix the 2 parts with nuts, bolts and rings

Step 5e : the structure, fix the sides. / Fix the 2 pieces with a metal plate. Use 50 mm screws (6) / Fix the other side repeating all the 5 steps.	Step 6a : the table top / Cut the 195 mm planks

Step 6b / Place the pieces / Keep a 20 mm space under the borders	Step 6c / Drill, mill and screw along the same lines (70mm screws(32)).

Step 6d / Trace the sides with a 60° angle. / Ask an adult for an electric saw to make a better cut.	Step 7 : reinforce stability / Cut drill, mill and screw (50 mm screws (12)) the reinforcement planks.

Last step : use sand paper to soften the cuts and test the result.